THÔNG TIN TÓM TẮT VỀ NHỮNG KẾT LUẬN MỚI

CỦA LUẬN ÁN TIẾN SĨ

Tên luận án: 	Nghiên cứu xử lý tín hiệu sonar thụ động để nâng cao chất lượng phát hiện mục tiêu ngầm trong điều kiện thủy văn phức tạp

Chuyên ngành: 	Kỹ thuật ra đa dẫn đường

Mã số: 			9.52.02.04

Nghiên cứu sinh: 	Trần Phú Ninh

# Người hướng dẫn:       PGS.TS Trịnh Đăng Khánh

# TS Ngô Văn Huấn

#### Cơ sở đào tạo: 		Học viện Kỹ thuật Quân sự

NHỮNG KẾT LUẬN MỚI CỦA LUẬN ÁN:

Đóng góp mới của Luận án là nghiên cứu, ứng dụng, phát triển các thuật toán trường phối hợp thích nghi sử dụng trong hệ thống Sonar thụ động để phát hiện và định vị mục tiêu ngầm trong vùng biển nước nông điển hình của Việt Nam. Các đóng góp cụ thể:

- Nghiên cứu xây dựng mô hình biển và đánh giá các yếu tố ảnh hưởng đến chất lượng phát hiện, định vị mục tiêu sử dụng thuật toán xử lý trường phối hợp thích nghi DL đối với một vùng nước nông điển hình ở Việt Nam. Kết quả khảo sát chỉ ra những yếu tố môi trường truyền âm trong biển ảnh hưởng đến chất lượng phát hiện định vị mục tiêu trong Sonar thụ động với thuật toán DL, làm rõ thêm những giá trị của từng yếu tố gây sai số.

- Đề xuất thuật toán tải đường chéo cải tiến IDL trên cơ sở điều chỉnh véc tơ trọng số của thuật toán DL giúp cải thiện độ phân giải và tỷ số đỉnh trên nền (PBR) của hàm bề mặt hàm bề mặt trong phát hiện định vị mục tiêu cho Sonar thụ động sử dụng phương pháp trường phối hợp thích nghi.

| NGƯỜI HƯỚNG DẪN KHOA HỌC PGS. TS Trịnh Đăng Khánh | NGHIÊN CỨU SINH Trần Phú Ninh |
| --- | --- |

SUMMARY ON THE CONCLUSION OF DOCTORAL THESIS

Thesis topic:	Study on signal processing in passive sonar systems to improve the performance of underwater source detection in complex hydrological conditions.

Major:			Navigation Radar

Code:			9.52.02.04

Ph.D Student:	Tran Phu Ninh

Supervisor:		Ph.D/Assoc. Prof. Trinh Dang Khanh

Ph.D. Ngo Van Huan

Training Institutions:	Le Quy Don Technical University

MAIN RESULTS OF THE DISSERTATION

The important contribution of the thesis is the studies, applications and developments of adaptive matched field processing algorithms used in passive sonar systems to detect and localize targets in specific shallow water in Vietnam.  The detailed contributions can be summarized as follows:

- The study proposed ocean models and evaluated factors that influences on the performance of source detection and localization when using DL adaptive matched field processing algorithms in particular shallow underwater areas in Vietnam. The results pointed out acoustic propagation factors of ocean environment which effect the performance of source detection and localization in passive sonar system if applying DL algorithm. The results also demonstrated the specific value of parameters that causes inaccuracy in the localization.

- Suggesting an improved diagonal loading (IDL) algorithm that is based on the adjustments for weight vectors of DL algorithms to improve the resolution and peak background rate (PBR) of surface ambiguity in source detection and localization ịn passive sonar systems using adaptive matched field processing.

| SUPERVISOR Assoc.Prof. Trinh Dang Khanh | Ph.D Student Tran Phu Ninh |
| --- | --- |